## Slide 1
SGGS-IET / NANDED
DESIGN
A SERIAL
CONVERTER
RS232 to TTL Level Translation using MAX232 IC
SUBMITTED BY
Vivekanand Shivshankar Swami
DEPARTMENT
Electronics & Telecomm. Engg.
SEMESTER / YEAR
7th Sem · 2026-27
DRAWN BY
V. S. Swami
DATE
2026-27
SCALE
NTS
SHEET
1 / 10

## Slide 2
02 / 10
AB
ABSTRACT
TYPE: INTERNSHIP REPORT
STANDARD: EIA-232-F
IC: MAX232CPE
VCC: 5V (REG.)
A module that bridges the voltage gap between 5V TTL
microcontrollers and legacy RS232 serial equipment.
The MAX232 IC acts as the core transceiver, using an internal dual charge-pump to generate
±10V RS232 rails from a single 5V supply — requiring only four external 1µF capacitors.
Upstream power regulation is handled by an LM7805 linear regulator, converting a 12V DC input
to a stable 5V rail. The complete design — schematic, PCB layout, and 3D model — was produced
in KiCad EDA and verified via PSpice simulation.
NOTE:
This report documents a SETU project-based internship completed under the guidance of the
Department of Electronics & Telecommunications Engineering, SGGS-IET Nanded.
DWG: ETL-232-02

## Slide 3
03 / 10 — SCOPE OF WORK
PROJECT OBJECTIVES
6 OBJECTIVES
01
Design a TTL↔RS232 level converter using
the MAX232 integrated circuit
02
Design a regulated 5V power supply using
the LM7805 voltage regulator IC
03
Verify the power supply circuit
performance through PSpice simulation
04
Simulate and validate the TTL-to-RS232
converter in PSpice with measured outputs
05
Draw the complete schematic and PCB
layout in KiCad EDA
06
Produce a compact, reliable module
suitable for serial communication
applications
DWG: ETL-232-03

## Slide 4
04 / 10 — VOLTAGE LEVEL TRANSLATION
THEORY OF OPERATION
+15V
+3→+15V
RS232 LOGIC 0
+3V
UNDEFINED
-3V
-3→-15V
RS232 LOGIC
1
-15V
RS232
5V
TTL HIGH
0V
TTL LOW
TTL
RS232 uses bipolar voltages — positive voltage for logic 0, negative for
logic 1. TTL uses 0V and 5V. These are incompatible; a direct connection
would damage microcontroller I/O pins.
The MAX232 contains two transmitters (TTL→RS232) and two receivers
(RS232→TTL). An internal charge pump circuit doubles and inverts the 5V
supply, creating the ±10V rails the RS232 transmitters need — with no
external power supply required.
SIGNAL PATH
TTL TX → T1IN → T1OUT → RS232
RS232 → R1IN → R1OUT → TTL RX
DWG: ETL-232-04

## Slide 5
05 / 10 — BLOCK DIAGRAM
CIRCUIT ARCHITECTURE
SYSTEM BLOCK DIAGRAM
INPUT
12V DC
Vin
REGULATOR
LM7805
+5V
TRANSCEIVER
MAX232
T1IN T1OUT · R1IN R1OUT
TX / RX
RS232 PORT
DB9 / Female
TTL 0–5V
DEVICE
MCU / PC
MAX232
Dual RS232 transceiver · DIP-16 ·
single 5V supply
LM7805
Linear voltage regulator · TO-220 ·
12V→5V
4× 1µF Caps
Charge pump network · C1+, C1−, C2+,
C2−
DB9 + Header
RS232 socket · 3-pin TTL connector
DWG: ETL-232-05

## Slide 6
06 / 10 — KICAD SCHEMATIC
SCHEMATIC DESIGN
KiCad EDA · Verified
POWER SECTION
12V DC input → LM7805 → 5V regulated rail
powering the MAX232 and TTL side
CHARGE PUMP
C1+/C1− (doubler) and C2+/C2− (inverter)
capacitor network generates ±10V RS232
rails internally
INTERFACE
T1OUT and R1IN routed to DB9 pins 2 and 3.
TTL side via 3-pin header (TX, RX, GND)
NOTE: All cap values 1µF / 16V. C5/C6 are supply
decoupling (10µF, 100nF).
DWG: ETL-232-06
FIG. A — MAX232 SCHEMATIC (KiCad)

## Slide 7
07 / 10 — PCB DESIGN
PCB LAYOUT & 3D RENDER
Ground plane on bottom layer for EMI suppression. All components through-hole for ease of
hand assembly.
3D view confirms component clearances and DB9 connector mechanical
fit.
DWG: ETL-232-07
FIG. B — PCB LAYOUT
2-LAYER · FR4 · 1.6mm
FIG. C — 3D RENDER
KiCad 3D VIEWER

## Slide 8
08 / 10 — BILL OF MATERIALS
LIST OF MATERIALS
8 ITEMS · REV A
S.NO.
COMPONENT
PART / VALUE
QTY
PACKAGE
01
RS232 Transceiver IC
MAX232CPE
1
DIP-16
02
Voltage Regulator IC
LM7805CT
1
TO-220
03
Capacitor — Charge Pump
1µF / 16V Electrolytic
4
Radial
04
Capacitor — Supply Filter
10µF / 100nF
2
Radial / 0805
05
RS232 Serial Connector
DB9 Female PCB-mount
1
THT
06
TTL Interface Header
3-Pin Male · 2.54mm
1
THT
07
Power Input Connector
2-Pin Screw Terminal 5mm
1
THT
08
Printed Circuit Board
Custom · KiCad
1
2-layer FR4 · 1.6mm
NOTES:
All capacitors rated minimum 16V. LM7805 heatsink recommended for Vin above 9V. Through-hole components only — suitable for hand soldering and
prototyping.
DWG: ETL-232-08

## Slide 9
09 / 10 — PSPICE RESULTS
SIMULATION & RESULTS
MEASURED OUTPUT VALUES
5.0V
REGULATED VCC OUTPUT
LM7805 output under
rated load — stable
±10V
RS232 RAIL SWING
Charge pump verified
120kbps
MAX DATA RATE
Per MAX232 datasheet
SIGNAL TRACE — SIMULATED
TTL IN
0V / 5V
RS232
±10V
SIMULATION FINDINGS
The LM7805 delivered a stable 5.0V output across all tested load
conditions. Ripple remained well within the 50mV limit specified in
the datasheet.
MAX232 charge pump operation confirmed: the doubler stage produced
+10V and the inverter stage -10V — sufficient margin above the RS232
minimum of ±3V.
Logic inversion was verified: TTL HIGH (5V) at T1IN correctly
produced RS232 SPACE (-10V) at T1OUT. The receiver path showed the
inverse behaviour on R1OUT.
Simulation tool: OrCAD PSpice · All component models sourced from manufacturer SPICE
libraries.
DWG: ETL-232-09

## Slide 10
10 / 10 — FINAL SUMMARY
APPLICATIONS & CONCLUSION
APPLICATIONS
Interfacing Arduino / STM32 with PC serial ports
Industrial automation — PLC and HMI communication
GPS receivers, barcode readers, legacy modems
Medical device data logging and serial telemetry
Embedded firmware debug consoles (UART over RS232)
CONCLUSION
This internship-based project delivered a complete, verified RS232-to-TTL converter
module — from first-principles voltage analysis through PSpice
simulation to a fabrication-ready KiCad PCB.
The MAX232-based design works reliably from a single 5V
supply with no external voltage rails. The KiCad workflow
produced a schematic, 2-layer PCB, and 3D render ready for
prototype fabrication.
STATUS
COMPLETE
INSTITUTION
SGGS-IET, Nanded · Dept.
of E&TC
STUDENT
V. S. Swami · Sem
7· 2026-27
DRAWN BY
V. S. Swami
DATE
2025-26
SCALE
NTS
SHEET
10 / 10